# L A M A R   C O U  N T Y

## Request For Bid

Bid No. RE-0522-3

## Return Deadline is NOT LATER THAN:  3:00 P.M., June 17, 2022

RETURN SEALED BID TO:

Lamar County Auditor

119 N. Main, Room B05

Paris, Texas  75460

### REQUEST FOR BID

5 – FORD F150S

FOR LAMAR COUNTY SHERIFF’S DEPARTMENT

- GENERAL INSTRUCTIONS TO VENDORS

- The Commissioner’s Court of Lamar County will receive bids until 3:00 P.M.,

Friday, June 17, 2022 for the purchase of a 5 new Ford F150s.

- Lamar County appreciates your time and effort in preparing a bid.  Please note

all bids must be received at the designated location by the deadline shown.  Bids received after deadline will be returned unopened and shall be considered void and unacceptable.  Opening is scheduled to be held in the Commissioner’s Courtroom, 1st Floor, Courthouse, Paris, Texas.

- The Commissioner’s Court reserves the right to reject any or all bids and to waive

minor technicalities.

- Bids should be sealed and labeled “BID – FORD F150s” and should be sent

to  the County Auditor’s Office, 119 N. Main, Room B05, Paris, Texas  75460.

- To obtain results, or if you have any questions, please contact the Lamar County

Auditor’s Office at (903)737-2416.

- Bids to be acceptable for consideration must conform to the following instructions

and specifications.

#### III.  SPECIFICATIONS

5 - FORD F150S

Specifications:	The 5 Ford F150s requested shall include the specifications included on the following pages.

Can Meet or Exceed These Specifications			 ______YES _____NO

###### STATE ORIGINAL PURCHASE PRICE: $_____________________________________________

STANDARD WARRANTY:

Describe standard warranty:__________________________________________________

_________________________________________________________________________

_________________________________________________________________________

DELIVERY TIME:__________days

BIDDER DOES (   )  DOES NOT (   ) MEET ALL SPECIFICATIONS

EXCEPTIONS:___________________________________________________________________

____________________________________________________________________

____________________________________________________________________

ADDITIONAL INFORMATION ON AVAILABLE LOADER: _________________________________ ______________________________________________________________________________________________________________________________________________________________

FIRM / BIDDER:__________________________________________________________________

BY:____________________________________________________________________________
	SIGNATURE								TITLE

ADDRESS:______________________________________________________________________

_______________________________________________________________________________

PHONE:_______________________________________   DATE:__________________________

Vehicle Specifications

Including Upfit

2022 Ford Responder

Lamar County Sheriff

1) 2022 OR 23 FORD F-150 RESPONDER POLICE PACKAGE, GAS

ENGINE (NON-HYBRID) WHITE

2) PUSH BUMPER WITH HEADLIGHT WRAPS

3) ONE RED/WHITE LED, ONE BLUE/WHITE LED MOUNTED ON CENTER

CROSSBAR OF PUSH BUMPER THAT GOES STEADY WHITE WITH

TAKEDOWN

4) FLASH HEAD AND TAIL LIGHTS

5) LIGHTBAR WITH RED / BLUE TO THE FRONT, FULL FRONT TAKE

DOWN. RED / BLUE TO REAR, WITH AMBER TRAFFIC ADVISOR.

6) SIREN AMP

7) CONTROLLER WITH 3 SLIDE SWITCH AND AT LEAST 6 OUTPUT

PUSH BUTTONS

8) SIREN SPEAKER (MOUNTED ON PUSH BUMPER)

9) (2)RED/BLUE LED MOUNTED IN REVERSE LIGHT AREA

10) (2)RED/BLUE LED MOUNTED ON LICENSE PLATE BRACKET

11) LICENSE PLATE BRACKET

12) (2)RED/BLUE SPLIT COLOR DUAL LIGHTHEAD LED TO MOUNT IN

UPPER BACK WINDOW

13) PARTITION BEHIND FRONT SEAT WITH SLIDING WINDOW AND

EXPANDED WIRE MESH IN WINDOW

14) DUAL GUN RACK MOUNTED ON PARTITION

15) 24” X 10” CONSOLE WITH DUAL CUP HOLDER, POWER STRIP,

AND ARMREST AND FACEPLATES FOR OTHER EQUIPMENT

16) TWO MIC CLIPS

17) ONE MAGNETIC MIC WITH A RISER MOUNT

18) STALKER DSR - Ka BAND DUAL ANTENNA RADAR

19) COMPUTER TABLET WITH FOLLOWING MINIMUMS (11.6” SCREEN,

WINDOWS 10, INTEL CORE i5-8650U VPRO 8TH GEN, 1.9 GHz TO 4.2

GHz PROCESSOR 8MB CACHE, MEMORY OF 1 SLOT 8GB UP TO 16

AND 128GB STORAGE)

20) TOUGH KEYBOARD (MOUNTED SEPARATE FROM TABLET)

21) DASH MOUNT FOR TABLET

22) KEYBOARD MOUNT SEPARATE FROM TABLET

23) MINIMUM 4G CAPABLE MOBILE ROUTER. FIRST NET READY AND

BAND 71 CAPABLE

24) WATCHGUARD 4RE IN CAR CAMERA SYSTEM WITH WiFi

DOWNLOAD

25) DECKED SYSTEM BED CARGO BOX

26) HD REAR REPLACEMENT BUMPER WITH WHITE INTEGRATED

SCENE LIGHTS

27) KENWOOD VHF CONVENTIONAL P-25 DIGITAL RADIO 110 WATT

28) KENWOOD UHF CONVENTIONAL P-25 DIGITAL RADIO 50 WATT

29) INSTALLATION KIT

30) LABOR

31) GRAPHICS

32) TINT

33) DELIVERY

ALL EMERGENCY LIGHTING, SIREN AND RELATED CONTROLS AND EQUIPMENT SHOULD BE WHELEN OR EQUIVELANT

DESKS, PARTITIONS, MOUNTING AND DOCKING EQUIPMENT SHOULD BE HAVIS, JOTTO, C-TECH, SETINA OR EQUIVELANT

PUSH BUMPER SHOULD BE ROUGHNECK, RANCH HAND OR EQUIVELANT